## Slide 1: Amateur Radio over IP and Digital Voice Modes
A rundown of Voice/Radio over IP, VHF/UHF Digital Voice modes and Solving the Tower of Babel
Tony Langdon VK3JED

## Slide 2: Contents
Early VoIP/RoIP Experiments (1995-2001) – Iphone, Speak Freely.
Analogue RoIP
  IRLP
  EchoLink
  AllStar
VHF/UHF Digital Voice (involved from dates given).
  D-STAR (2007 - ).
  DMR (2014 - ).
  System Fusion (2020 - ).
  M17 (2021 - ) First fully open VHF/UHF DV.
  Hotspots/Gateways.
DMR
M17
VK Multimode Network.
  Origins and Experiments.
  Current Structure and Capabilities.
Questions.

## Slide 3: Early VoIP/RoIP Experiments
1995 – 2001 Internet Phone (Iphone)
  Early closed source Windows VoIP software. Came into use on Amateur Radio from the mid 1990s.
  Repeaters linked from mid 1990s, companion app sometimes used as directory and to limit access to licenced Amateurs.
  Australia Day 2001 – Experimental national hookup of repeaters around Australia. I ran a link in Melbourne.
1995 – onwards Speak Freely
  Flexible open source VoIP software for Windows and Linux, originally repeased in the public domain.
  Became the basis for IRLP in 1997, when Dave Cameron VE7LTD was looking to improve on the Iphone experiments.

## Slide 4: Analogue RoIP
Internet Radio Linking Project (1997 - ).
  First Amateur specific RoIP system, based on a modified version of Speak Freely.
  Built on Linux for stability.
  Access only via Radio gateways (simplex or repeater).
EchoLink (2002 - ).
  Windows based RoIP system, allows RF or direct access via PC/Smartphone.
  Originally an improved client for iLink, but quickly became its own network.
  Software for Linux and other platforms available.
AllStar (early 2000s - )
  Built around an early version of Asterisk open source PBX on Linux.

## Slide 5: VHF/UHF Digital Voice – Personal history.
Dates given are roughly my first involvement.
D-STAR (2007 - ).
DMR (2014 - ).
Yaesu System Fusion (2020 - ).
M17 – Fully Open DV (2021 - ).
Hotspots/Gateways
  DV-RPTR (early 2010s).
  OpenSpot 1 (mid 2010s - ).
  MMDVM/MMDVM Hotspot (2020 - ).

## Slide 6: DMR
DMR is a commercial mode that has been repurposed for Amateur Radio use, and several DMR networks now exist. Amateur use of DMR is Tier II (conventional TDMA).
Common DMR networks include:
Brandmeister (the most popular outside of VK).
VK-DMR/DMR+ (Popular in VK).
FreeDMR.
FreeSTAR.
  IPSC2.
  System-X.
TGIF.
Others.
Demonstration.

## Slide 7: M17
M17 is the first mode to be built from the ground up by the wider Amateur Radio community, and is also the first completely open VHF/UHF DV mode. All software/firmware components as well as hardware implementations are completely open and able to be reproduced by anyone. M17 features include:
100% open source and open standard, including vocoder (Codec2 3200/1600).
Full rate voice, half rate voice/data and packet (data only modes).
Simplified callsign based addressing (similar to D-STAR, but easier to use).
Optional encryption (useful for EMCOMM where allowed).
Vibrant open source community!

## Slide 8: M17
Implementations for users.
IP Access
  DroidStar (Linux/Windows/Android/iOS).
  mvoice (Linux).
RF Clients
  M17Client (Linux).
    + MMDVM + Data capable radio(s).
    + MMDVM Hotspot.
  TNC3/4 + Data capable radio.
  M17tools + Data capable radio.
  Modified MD-380/MD-380UV/RT3/RT3S with OpenRTX firmware.
  Module17 + Data capable radio.

## Slide 9: VK multimode network – origins.
First stage – IRLP reflector 9550-9559 (2009 - ).
Originally built in 2009 to facilitate development of second generation IRLP/EchoLink integration.
D-STAR Reflector REF023 installed in 2009, still runs on site.
Second stage – Experimental multimode DV reflector.
Started in 2020 as a COVID-19 lockdown project.
Ran on two virtual servers with transcoders on one server, reflectors and AllStar node on the other.
Became the core of the Pride Radio Network in 2021.
Supported a single (Pride Radio) network using EchoLink, AllStar, YSF, D-STAR, NXDN, P25 and M17, with a link to IRLP 9550.

## Slide 10: VK Multimode Network – Structure and Capabilities.
Main transcoder and AllStar/DV reflector hub was rebuilt on a new server using Docker for most components. This allowed the two servers to be consolidated into one and the design is more modular. Adding new networks is a fairly straightforward process of combining individual components (which run in Docker containers) to build the new network.
Currently supports 8 independent networks of varying configurations and mode capabilities. Each network is individually configured to meet its needs. Links to IRLP network use USRP instead of RTP for reliability.
System information can be found at https://vkmultimodenetwork.weebly.com .

## Slide 11: Questions?
Links
IRLP https://www.irlp.net/
EchoLink https://www.echolink.org/
AllStar https://www.allstarlink.org/
FreeDMR https://www.freedmr.uk/
FreeSTAR https://freestar.network/
M17 Project https://m17project.org/
VK Multimode Network https://vkmultimodenetwork.weebly.com/